## Slide 1: Giới thiệu sản phẩm nội soi parcus - anika

## Slide 2: Parcus Acquisition – anika mua lại parcus
Anika mua lại Parcus Medical LLC – 01/2020
Về công ty Parcus:
  Thành lập năm 2007
  Các sản phẩm nội soi:
      Nội soi vai - Shoulder
      Gối - Knee
      Háng - Hip
      Kết hợp xương - Distal Extremities
  Sản phẩm được sản xuất tại Mỹ với chất lượng cao và luôn luôn cải tiến
  Có hơn 400 sản phẩm
  Có mặt tại hơn 40 quốc gia
Notes: $35m + $60m

## Slide 3: Vít chỉ neo - knotted anchors (Preloaded)
Được sử dụng trong nhiều phẫu thuật khác nhau và là một trong những kiểu neo linh hoạt nhất.
Dùng trong:
  Tất cả các khớp
Vật liệu:
  Titanium
  PEEK
  PEEK CF
  Vít tự tiêu - Biocomposite (absorbable)
  Chỉ - All-Suture (soft)
Có thể lắp sẵn với:
  Chỉ - Suture
  Chỉ dẹt - Tape
Kích cỡ vít:
Mất vững - Instability sizes = 1.8mm – 3.5mm
Rách chóp xoay - Rotator cuff sizes = 3.2mm – 6.5mm
nội soi vai

## Slide 4: VÍt neo - Shoulder Anchors
Đa dạng - Wide variety
Kích thươcnsg từ 1,8mm đến 6,5mm - Sizes ranging from 1.8mm up to 6.5mm
Có chỉ, không chỉ và hỗn hợp - Knotted, knotless, hybrid
Chỉ số 2, chỉ dẹt 1,6mm, chỉ dẹt 2mm - #2 suture, 1.6mm suture tape, 2mm suture tape
Chất liệu:
  Titanium
  PEEK
  PEEK CF
  Biocomposite

## Slide 5: VÍT CHỈ NEO - Knotted anchors
V-LoX Titanium
V-LoX PEEK CF
Twist PEEK
Twist Biocomposite

## Slide 6: VÍT CHỈ NEO - Knotted anchors
Draw Tight
PEEK CF Push-In
X-Twist
X-Twist

## Slide 7: VÍT NEO - Knotless anchors
X-Twist
Knotless PEEK CF
Knotless AP
Twist Knotless

## Slide 8: V-lox Titanium VÍT CHỈ NEO - Knotted anchors
Sizes: 4.5, 5.0, 5.5, 6.5mm Vật liệu - Material: Titanium
Mỏ neo ngựa - Workhorse anchor
Sử dụng dễ dàng và tin cậy - Quick, easy and reliable
Độ bền và ổn định cao - High strength and stability
Ren toàn bộ thân giảm thiểu nguy cơ bị kéo ra - Fully threaded reduces risk of pull-out
Tiết kiệm bước ren giảm thiểu khoan nhiều xương - Step saving by minimising bone preparation
Thiết kế có hoặc không có kim - With or without needles
Được lắp sắp với chỉ số 2 - Pre-loaded with #2 sutures
Có thể 2 chỉ hoặc 3 chỉ - Double or triple loaded

## Slide 9: V-lox PEEK CF VÍT CHỈ NEO - knotted anchors
Sizes: 5.5, 6.5mm Vật liệu - Material: PEEK CF
Sản phẩm đầu tiên thuộc nhóm vít chỉ neo được làm từ vật liệu sợi các bon và PEEK OPTIMA - First family of suture anchors manufactured from carbon fiber reinforced PEEK OPTIMA
Chủ yếu được dùng cho khớp lớn - Primarily used in larger joints
Ren toàn bộ thân giảm thiểu nguy cơ bị kéo ra - Fully threaded reduces risk of pull-out
Thiết kế có hoặc không có kim - With or without needles
Được lắp sẵn với chỉ số 2 hoặc chỉ dẹt 1,6mm - Pre-loaded with #2 sutures or 1.6mm suture tapes
Có thể 2 chỉ hoặc 3 chỉ - Double or triple loaded
An toàn, tương thích sinh học, cản quang - Safe - Biocompatible, radiolucent, MR safe, inert

## Slide 10: Vật liệu? PEEK CF - what is it?
Vật liệu Polyetheretherketone được gia cố bằng sợ các bon - Carbon fiber-reinforced Polyetheretherketone (PEEK)
  Sợi carbon ngắn được phân tán trong vật liệu PEEK tự nhiên - Short carbon fibers dispersed within natural PEEK
  Có màu đen bóng - Glossy black finish
  Tăng độ cứng và chắc chắn hơn vật liệu PEEK tự nhiên - Increased stiffness and strength over natural PEEK
  Có sẵn với các tỉ lệ sợi các bon khác nhau - Available in varying percentages of carbon fiber
    Parcus độc quyền với tỉ lệ 30% sợi các bon - Parcus exclusively uses 30% carbon fiber PEEK
Dùng trong y tế - Used in Medical Devices
  Không xê dịch, bất động - Inert
  Khả năng chống mài mòn cao - Excellent wear resistance
  Tương thích sinh học - Biocompatible
  Cản quang và an toàn - Radiolucent and MR safe
  Chứng chỉ FDA/CE
  Được sử dụng hơn 20+ years

## Slide 11: ĐẶC TÍNH VẬT LIỆU - PEEK CF - MATERIAL PROPERTIES
Elastic Modulus
How much pressure can be applied before the material permanently deforms
Example: paperclip bends and returns to its normal shape up until its elastic modulus is exceeded
Tensile Strength
How much pressure the material can take before it breaks
Example: pencil snaps in half once the tensile strength is exceeded

## Slide 12: Peek cf - advantages
2x stronger than PEEK
Excellent performance for interference screws
Capable of insertion into very hard bone
Self-punching in some instances
Closer mechanical properties to cortical bones than other materials
Bone is neither weakened nor stressed after implantation
Bone-life stiffness may reduce the occurrence of stress shielding whilst enhancing bone healing
Safe
100% inert
Easily removable in revision surgeries
Proven biocompatibility to ensure safe long-term implantation
Radiolucent on X-Rays and CT Scans, and MR safe

## Slide 13: Twist knotted anchors
Sizes: 4.5, 5.5, 6.5mm Material: PEEK or Biocomposite
Widest variety of configurations
  PEEK or Biocomposite material
  With or without needles
  Double or triple loaded
  #2 suture, 1.6mm suture tape, 2mm suture tape
Fully threaded design provides optimal cortical fixation which reduces the risk of pull out
Great option for streamlined repair

## Slide 14: Twist SST knotted anchors
Sizes: 4.5, 5.5, 6.5mm Material: PEEK or Biocomposite
Pre-loaded with a non-sliding, locked in, 2mm suture tape
Allows for true knotless repair
Single handed insertion vs. competitors options
Tape handles better than competitors’
Slack taken up by the lateral row = easier & consistent tensioning
Eliminates knot tying, and potential knot irritation

## Slide 15: Draw tight knotted anchors
Sizes: 1.8, 3.2mm Material: UHMWPE + PEEK
Soft vs. hard anchors
Safe
Bone sparing
Revision friendly
Allow for multiple points of fixation
Work on expansion after insertion

## Slide 16: Draw tight knotted anchors
Sizes: 1.8, 3.2mm Material: UHMWPE + PEEK
Deployable Suture Based Anchor
Two sizes
Unique Deployment Suture that provides tactile feedback for positive fixation
PEEK Power tip for improved insertion and solid core for stronger fixation
Preloaded with Suture or Suture Tape
Distal extremity option with needles

## Slide 17: Draw tight knotted anchors
Sizes: 1.8, 3.2mm Material: UHMWPE + PEEK
PEEK Power Tip
Improved insertion vs. nitinol fork of direct competition
Provides solid core translating to stronger fixation

## Slide 18: Draw tight knotted anchors
Sizes: 1.8, 3.2mm Material: UHMWPE + PEEK
White deployment sutures
Unique among all-suture anchors
Provides tactile feedback for positive fixation
Ability to utilize static deployment sutures
One of the shortest drill depth of any suture based labral anchor (19mm)
Size of the suture ball after deployment?
1.8mm Draw Tight ~ 3.5mm, 3.2mm Draw Tight ~ 5.5mm

## Slide 19: Peek cf push-in Knotted anchors
Size: 3.5mm Material: PEEK CF
Simple push in anchor with high pull-out strength
With or without needles
Loaded with #2 suture or 1.6mm suture tape
PEEK CF material
Strength to find glenoid hole
Modulus of elasticity matches bone reducing stress on glenoid

## Slide 20: Knotless anchors
Newer technology compared to knotted (pre-loaded) anchors
Not preloaded with suture
Can be used in:
  All joints
Can be made from:
  Titanium
  PEEK
  PEEK CF
  Biocomposite (absorbable)
  All-Suture (Soft)
Can be loaded with
  Suture
  Tape
Instability sizes = 2.8mm – 3.5mm
Rotator Cuff sizes = 3.5mm – 6.25mm

## Slide 21: Knotless PEEK CF knotless anchors
Sizes: 2.8, 3.5, 4.5, 5.5mm Material: PEEK CF
Strong solid piece design
Self punching for most rotator cuff repairs
PEEK CF material
Large eyelets to accommodate multiple suture configurations
Simple and reproducible technique for instability and rotator cuff repair
Modulus of elasticity closely matching cortical bone
Eco-friendly & cost-effective re-usable handle option

## Slide 22: Knotless PEEK knotless anchors
Size: 2.8mm Material: PEEK
Strong solid piece design
PEEK material
Can accommodate suture or tape
Simple and reproducible technique for instability
Non-absorbable, radiolucent, MR safe
Available in standard and hip length

## Slide 23: Knotless AP knotless anchors
Sizes: 2.8, 4.5, 5.5mm Material: Advanced Polymer
Advanced Polymer
  70% PLGA – Biocompatible, absorbable and comprised of naturally occurring compounds
  30% ß –TCP – Osteoconductive and facilitates adhesion of osteoblasts, and supports bone integration and ingrowth
Resorbable, radiolucent, MR safe
Strong solid piece design
Large eyelets to accommodate multiple suture configurations
Simple and reproducible technique for instability and rotator cuff repair

## Slide 24: Twist knotless knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Eliminates possibility of over tensioning repair
  Sutures run along anchor and up center of anchor, instead of alongside
Strong solid piece design
Inserter nose to help with axial alignment
Single handed insertion
Accommodates multiple sutures/tapes
Simple and reproducible technique for rotator cuff repair
Short handled option for distal extremities

## Slide 25: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Versatile
Strong
Supports healing
Quick & easy to use
4.75mm
5.5mm
6.25mm

## Slide 26: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Sliding
True Surgical Freedom
Intra-operative flexibility
One product that allows for multiple techniques
Knotless anchor that can be used like a knotted anchor
  Load sutures through distal eyelet
Knotted anchor
  Preloaded with sliding suture or tape/s

## Slide 27: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Large Distal Eyelet
Accommodates four 2mm tapes & three #2 sutures
Maximise tendon to bone coverage
Versatility in repair constructs
Conical tip for easy placement

## Slide 28: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Multiple Sliding Suture Configurations
Preloaded with sliding:
  1 x #2 suture
  1 x 1.6mm suture tape
  2 x 1.6mm suture tapes
Sliding

## Slide 29: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25 Material: PEEK
Double Helix Design
2 independent threads in a double helix relationship
Fast insertion
Easy-in double start thread
3 ¼ turns
Notes: Arthrex SwiveLock = 8 turns

## Slide 30: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Open Architecture Design
1.4mm vents run along four sides
Maximally cannulated
Promotes marrow element flow to repair site
Supports healing
Bony ingrowth
Notes: Less material
Bone marrow density around the anchor

## Slide 31: X-Twist knotless anchors
Sizes: 4.75, 5.5, 6.25mm Material: PEEK
Superior Anchor Driver Interface Geometry
X-Spline™
Exceptional performance
High torque capability
Reliable insertion even in hard bone
2 x Torsional efficiency vs. traditional hex design
X-Spline Driver vs Traditional Hex Design
2 x torsional efficiency
46% reduction in total anchor loading
56% reduction in radial loading

## Slide 32: X-Twist knotless anchors
Smart Thread Design
Buttress thread
Easy insertion
Improved pull-out
Fully threaded
Cortical and cancellous fixation
Strength and rigidity
Sizes: 4.75, 5.5, 6.25 Material: PEEK
Tailing edge resists pull out
Leading edge facilitates insertion

## Slide 33: X-Twist knotless anchors
  Stable Tip for reproducible tensioning
X-Spline™
  Unique X-Spline Drive Geometry for maximal torsional efficiency
  Abundant Tape Holding Capacity
  More Sliding Suture/Tape Options
  Easy-In Double Start Thread Design
  Maximally Fenestrated on 4 sides for marrow flow and bony ingrowth
  Smart Buttress threads for easy insertion and improved pull out
  Double Helix Threads for fast insertion
  Tapered Tip for easy placement

## Slide 34: Shoulder repair Continued

## Slide 35: Parcus braid
28 suture SKUs and growing
High Picks Per Inch (PPI) = low friction
Whipstitching grafts
Pull-through sutures
Traction sutures
Knotless anchor repairs
Suture augment (“Internal Brace”)
Infinity Loop sutures and tapes
Singles or Boxes (6/12)
Suture options: #1, #2, #5 Material: UHMWPE
Tape options: 1.6mm, 2mm
Needle options: CE, MO-6, CCS, Straight

## Slide 36: Shoulder arthroscopy instruments
Complete system for shoulder arthroscopy
Penetrating Grasper
Clever Hook
Sixter
Suture Manipulator
Tissue Grasper with Ratchet
Forked Tissue Grasper
Tape Multi-Suture Cutter
Anika Sports Medicine Instruments

## Slide 37: PTS Passer
Parcus Tape & Suture Passer
Reliable passer able to pass through thick cuff tissue
Easy to use with side loading design
Active window, trap door
Able to fit down 6.5mm cannula
Ratchet and non-ratchet handles available
Single use disposable needle

## Slide 38: Biceps repair

## Slide 39: Biceps Repair
SLiK Fix
Actiflip Cinch
Actiflip Whip

## Slide 40: SLIK FIX Biceps tenodesis
Sizes: 7, 8, 9mm x 15mm Material: PEEK CF & PEEK
Proximal biceps tenodesis system
Supra-pectoral or sub-pectoral
Activation button allows for one-handed operation and insertion
Suture retention tip and tendon washer control suture and protect graft
Time saving
Designed to advance tendon in socket prior to compression
PEEK CF material

## Slide 41: Actiflip cinch Biceps tenodesis
Button Dimensions: 3.2mm x 10mm Material: Titanium & UHWMPE
Ideally suited for proximal biceps
  Sub or supra pectoral
Mini/open
Unicortical or Bicortical fixation
AcTiFlip activation button allows for reliable deployment
Unique cinch loop
  Protects tendon
  Eliminates need to fully whipstitch
  Precise control & tension
  Loaded with needles & #2 suture
Retractable finger allows for reloading of button

## Slide 42: Actiflip whip Biceps tenodesis
Button Dimensions: 3.2mm x 10mm Material: Titanium & UHWMPE
Ideally suited for distal biceps repair
  Can also be used for open proximal biceps (sub/supra)
Mini/open
Unicortical or Bicortical fixation
AcTiFlip activation button allows for reliable deployment
  Naked button
  Pack includes #2 Infinity Loop with Straight Needle
Tension slide to dock tendon
Retractable finger allows for reloading of button

## Slide 43: Knee repair

## Slide 44: Suspensory devices
GFS Ultimate | GFS Mini | GFS Large II | GFS BTB Link

## Slide 45: Interference screws
Titanium | PEEK CF | Biocomposite

## Slide 46: GFS Ultimate ACL fixation Adjustable Loop
Sizes: Micro, Mini & Large Material: Titanium & UHMWPE
Adjustable loop ranging from 12mm to 60mm
Convenience of adjustability with strength of fixed loop devices
Leading and toggle sutures to confirm deployment
Adjustment suture allows for single handed reduction
Graft sleeve to protect graft during tensioning
  Allows for different graft preparation techniques
GFS Ultimate Micro = 3.2mm x 12mm
GFS Ultimate Mini = 3.9mm x 12mm
GFS Ultimate Large = 3.9mm x 16.5mm
  Backup/revision option
  Allows for easy quadrupled semi-tendinosis ACL

## Slide 47: GFS Mini ACL Fixation Fixed Loop
GFS Mini
Titanium button – 3.9 x 12mm
UHMWPE loop – 12-55mm
White leading suture - #5
Black/white flipping suture – #2
GFS II
Revision & backup button option for cortical blowouts
Titanium button - 4.4mm x 16.5mm
UHMWPE loop – 12-45mm

## Slide 48: GFS BTB Link ACL Fixation
To be combined with GFS family*
  GFS Mini
  GFS II
  GFS Ultimate
Allows for linking of GFS family to varying grafts
Simpler than competitive devices
True intra-operative flexibility
*Can also be used with competitor loops
Button: 2.4 x 8mm Loop: 15mm Material: Titanium & UHMWPE

## Slide 49: GFS Naked ACL Fixation
Nano = 1.4 x 5.9mm
Micro = 2.0 x 8.0mm
Mini = 3.9 x 12mm
Standard = 3.9 x 14mm
Large = 4.4 x 16.5mm
XL = 4.4 x 21mm
Can also be used in Shoulder and Distal Extremities
Unicortical or bicortical fixation
Backup fixation
Multiple suture holes
Button Dimensions Material: Titanium

## Slide 50: Interference Screws ACL Fixation
Naturally lubricious, minimises graft locking
Fully threaded for optimal fixation in soft tissue & BTB grafts
Non-absorbable, radiolucent, and MR safe
Rounded edges to protect soft tissue grafts
Driver is tapered and square, distributes torque
Provides the strength and stiffness required for successful ligament reconstruction
Fully threaded for optimal fixation in soft tissue & BTB grafts
Rounded edges to protect soft tissue grafts
PEEK CF Sizes: 7-12mm x 20-35mm
Titanium Sizes: 7-12mm x 20-35mm

## Slide 51: B-Screw ACL Fixation
Polyal®
  70% PLA [poly(70/30; L/DL)lactide]
  30% ß-TCP [beta tricalcium phosphate]
Homogenous mix
Soft tissue & bone tendon grafts
Ligament reattachment
Double thread design
Self tapping
High torque resistance
Screw supported internally by driver
Material: Biocomposite Sizes: 6-11 x 20-35mm
35mm 30mm
24mm 20mm
6mm
7mm
8mm
9mm
10mm
11mm

## Slide 52: Distal extremity repair

## Slide 53: Synd-Ez knotless syndesmosis repair
Length of Construct: 85mm Material: Titanium & UHMWPE
Versatile design
Use with or without fracture plate
Washer included for use without fracture plate
Top hat is low profile and self centering
Convenience pack
Adjustable knotless construct
Simplifies surgical procedure
Single adjustment suture
Counter traction suture and tension handle
Integrated for predictably smooth tension of construct

## Slide 54: Miti knotted anchors
Sizes: 2.0, 2.5, 3.0, 3.5mm Material: Titanium
Quick, easy and reliable
High strength and stability
Fully threaded reduces risk of pull-back
Step saving by minimising bone preparation
Size specific k-wire packaged with each anchor
Pre-loaded with 3-0 or #2 suture
With or without needles
XL version for shoulder repair

## Slide 55: ATLAS CMC Reconstruction
Anchor: 1.8mm Material: UHMWPE & Titanium
Button: 2.0 x 8.0mm
Anatomic Thumb Ligament Arthroplasty System
Strong, stable, bone sparing
Convenience pack
Suspensory arthroplasty
Does not require a tendon graft harvest
Small insertion footprint
Sub-cortical fixation
Single incision approach

## Slide 56: Miscellaneous

## Slide 57: Pin packs Acl Reconstruction
1.1 & 1.5mm Pin Packs
High volume opportunity
Low maintenance product
Door opener
Consists of
2.4mm x 42cm Drill Tip Guide Pin with Eyelet
2.4mm x 32cm Drill Tip Guide Pin
1.1mm or 1.5mm x 300mm Nitinol Guide Wire

## Slide 58: Parcus shoulder traction kit Patient positioning
Size: Universal Unit of Measure: 6 per box
Quick, easy and reliable
Provide a convenient method to apply traction and position patient's arm
Used with Parcus Traction Unit or competitors’ towers
Simple convenience pack
Includes: Stockinette, Strap Roll, Rope & S-Hook
Low maintenance
Door opener

## Slide 59: GPS Patient access
Guide Pin System
Hip arthroscopy
Used to establish and switch portals
High volume opportunity
Low maintenance product
Door opener
Consists of
2 x 1.1mm Nitinol Guidewire
2 x 17 gauge needles